## Slide 1
PPT-PRIORITY COMPLETION
The original two-plane + two-ellipse measurement pipeline is complete.
Population measurements and statistics are finished across the available cohort. The generative model is intentionally deferred.
200
NIfTI labels
programmatically discovered
191
complete cases
two planes + two ellipses
77,337
point residuals
source vs ellipse records
0.0 mm
source change
coordinates and segments
PRE-GENERATION BOUNDARY
No synthetic vessels
were created.
Source: measured PPT-priority outputs • generator deferred
01

## Slide 2
SOURCE OF TRUTH
One pipeline governs the work — and this increment stops at statistics.
200 NIfTI
labels
→
centerlines +
landmarks
→
2 SVD
planes
→
2 fitted
ellipses
→
population
statistics
STOP
before
generation
Original PPT work = primary
Heart-support surface = preserved extension
This deck reports measured evidence only. Parameter sampling, synthetic control points, noise sampling, generated bifurcations, B-splines and real-vs-generated comparisons remain outside this increment.
Source: measured PPT-priority outputs • generator deferred
02

## Slide 3
REUSE, NOT RESTART
Good extraction and geometry code was reused; the PPT gaps were filled independently.
REUSED
• NIfTI discovery and label adapter
• LMCA/LAD/LCX extraction
• multi-signal RAS daughter assignment
• inferred RCA candidate logic
• centroid-SVD plane utility
• exact source landmark/endpoints
ADDED FOR PPT DEFINITION
• deterministic population RAS plane basis
• all-support actual 2-D ellipse fit
• fixed theta and axial tilt conventions
• branch angular extents on ellipse
• signed per-point residual table
• robust, circular and correlation statistics
Protected outputs were hash-checked before and after the run: Stage-1 VTK scaffold and parametric heart surface remained unchanged.
Source: measured PPT-priority outputs • generator deferred
03

## Slide 4
METHOD SEPARATION
SVD answers “which plane?”; ellipse fitting answers “which a, b and tilt?”.
A — SVD PLANE
source XYZ → centroid → SVD
Outputs
centroid
normal
plane basis
point-to-plane residual
does not output a, b or tilt
B — ACTUAL ELLIPSE
plane (u,v) → nonlinear 2-D fit
Outputs
center
semi-major a
semi-minor b
axial tilt + fit residual
lifts back to 3-D only for reference/visualization
→
The source coordinate array is copied, measured and hash-verified. It is never snapped to either object.
Source: measured PPT-priority outputs • generator deferred
04

## Slide 5
COHORT RESULT
191 of 200 label volumes complete both planes and both ellipses.
Nine cases retain the existing documented failure: no bifurcation satisfied Stage-2 LCA selection thresholds.
191
eligible cases
95.5% of discovered
Source: measured PPT-priority outputs • generator deferred
05

## Slide 6
TWO PLANES / PATIENT
The crown and LAD planes retain distinct anatomical roles.
Crown support: LCX + inferred RCA candidate where available. LAD plane: unchanged LAD descent. RCA remains candidate—not annotated ground truth.
189
inferred RCA support
2 LCX-only approximations
Source: measured PPT-priority outputs • generator deferred
06

## Slide 7
TWO ACTUAL ELLIPSES
Each projected support set is fit by a genuine planar ellipse — never by the SVD display patch.
The source arteries remain unchanged. Ellipse curves are statistical references measured in their fitted planes.
2 × 191
actual ellipse fits
all unchanged source support
Source: measured PPT-priority outputs • generator deferred
07

## Slide 8
ELLIPSE PARAMETERS
Partial arterial arcs create long-tailed full-ellipse parameters — the tails stay visible.
55.2 mm
crown a median
mean 90.8 • long upper tail
198.5 mm
LAD a median
mean 215.0 • partial-arc fit
Scientific handling
No cases were removed simply to lower RMSE. Mean, median, IQR, P5 and P95 expose fit instability transparently.
Source: measured PPT-priority outputs • generator deferred
08

## Slide 9
ANGLE CONVENTION
A deterministic RAS-tied frame removes arbitrary axis signs from population theta.
θ = 0
+ minor axis
major axis e₁
1
Plane u comes from projected RAS +X; +Y/+Z are deterministic fallbacks.
2
Normal sign uses fixed RAS Z/Y/X priority, producing a right-handed frame.
3
Ellipse major axis is axial: tilt lives in [−90°, 90°); theta increases toward +minor axis.
This convention prevents 180° sign flips from corrupting population statistics.
Source: measured PPT-priority outputs • generator deferred
09

## Slide 10
LANDMARK THETA
Bifurcation and terminal positions are circular variables, not ordinary means.
Landmark theta has a 360° period. Circular mean, circular standard deviation and resultant length are exported.
360°
theta period
directional circular
Source: measured PPT-priority outputs • generator deferred
10

## Slide 11
BRANCH EXTENT
LAD and LCX extent is measured along the fitted ellipse, in source order.
LCX |extent| mean 54.1°. LAD |extent| mean 95.4°. Extent is unwrapped terminal theta minus initial theta—not a Euclidean bifurcation angle.
95.4°
mean LAD extent
LCX mean 54.1°
Source: measured PPT-priority outputs • generator deferred
11

## Slide 12
PER-POINT DEVIATION
77,337 point records preserve how vessels depart from ideal ellipses.
Each row stores normalized branch position, theta, source XYZ, reference XYZ, signed in-plane residual, signed out-of-plane residual and Euclidean residual.
10.66 mm
LCX mean point residual
LAD mean 2.99 mm
Source: measured PPT-priority outputs • generator deferred
12

## Slide 13
POPULATION STATISTICS
Every model variable carries robust summaries; angles also carry circular summaries.
CROWN
a 90.8 ± 127.8 mm
b 40.4 ± 15.9 mm
tilt μc 1.7° • σc 31.5°
LAD
a 215.0 ± 168.8 mm
b 69.0 ± 44.7 mm
tilt μc −29.0° • σc 68.0°
RELATION
plane angle 70.4 ± 15.3°
LCX extent 54.1 ± 35.7°
LAD extent 95.4 ± 71.5°
RESIDUAL
LCX mean 10.66 mm
LAD mean 2.99 mm
signed + Euclidean pooled
Each variable exports N • mean • sample SD • median • IQR • min/max • P5/P95 — plus circular mean, circular SD and resultant length where appropriate.
Source: measured PPT-priority outputs • generator deferred
13

## Slide 14
DEPENDENCE
Correlation is measured now so later sampling does not assume independence blindly.
Pearson r is a diagnostic for selected continuous linear quantities. Circular-linear dependence remains a later modeling decision.
Pearson r
diagnostic only
selected linear variables
Source: measured PPT-priority outputs • generator deferred
14

## Slide 15
SOURCE INTEGRITY
Measurement changed no source coordinate and no source segment length.
Max coordinate change: 0.0 mm. Max segment-length change: 0.0 mm. Per-array and per-archive SHA-256 hashes are stored.
0.0 mm
maximum change
coordinates + segments
Source: measured PPT-priority outputs • generator deferred
15

## Slide 16
EXTENSION SEPARATION
The later heart-support surface is preserved as an extension — not a substitute.
ORIGINAL PPT MODEL
two patient planes
two fitted planar ellipses
landmark theta + branch extent
per-point residuals
population statistics
PRESERVED EXTENSION
parametric 3-D heart support surface
Stage-1 VTK/VTM scaffold
Future combination is possible—but neither definition is rewritten to imitate the other.
Source: measured PPT-priority outputs • generator deferred
16

## Slide 17
NEXT INCREMENT
Generation begins with joint sampling; none of these future steps run today.
joint ellipse
parameter sampling
→
circular landmark
sampling
→
arc-length
control points
→
smooth empirical
residuals
→
shared LMCA
bifurcation
→
reuse B-spline +
validate
DEFERRED — no sampler, synthetic noise, generated vessel, B-spline output, VTK sample or real-vs-generated comparison exists in this increment.
The measured CSV/JSON files are the validated hand-off for this future work.
Source: measured PPT-priority outputs • generator deferred
17

## Slide 18
COMPLETION STATUS
The measured PPT model is ready for a later, separately validated generator.
200
labels discovered
9 documented extraction failures
191
two-plane fits
centroid-SVD in RAS
191
two-ellipse fits
all support points measured
191
population cases
robust + circular statistics
Delivered now
case status • per-patient parameters • pointwise residuals • statistics • circular summaries • correlation matrix • 12 modular figures • method/audit reports • this presentation
Next decision
Choose the joint/circular statistical sampling design, then implement and validate the generative model as a separate increment.
Generator status: NOT IMPLEMENTED BY DESIGN
Source: measured PPT-priority outputs • generator deferred
18